0512.4490 Advanced Computer Architecture Lab 2020
Lab #3: Verilog introduction

In this lab we'll learn to use Verilog simulation tools using simple examples.

Technical notes:
A. In order to compile Verilog sources, use the following command within the directory that contains all the *.v files:
ncverilog +access+rw *.v
B. In order to see the wave-diagram of the previous Verilog simulation use:
simvision waves.vcd

Assignments:
For each exercise, submit the verilog source files, a log of the testbench run, and a wave screenshot if requested.

1. Mux
The file mux.v contains two implementations of a 2:1 mux: the first using continuous assignment syntax, and the second using an always block. Both have the following inputs/output:

module mux1(a,b,select,result);
   input a;
   input b;
   input select;
   output result;

If select is '1', b is selected, otherwise a is selected.

Complete the code, and test it using the provided mux_tb.v testbench.

2. Half adder
Design a 1-bit half adder using structural gate level Verilog. The adder accepts two binary inputs: a and b, and computes their output sum and carry:

module halfadder(a,b,sum,carry);
   input a,b;
   output sum, carry;

The files halfadder.v and halfadder_tb.v contain a partial implementation for the half adder and its testbench. Complete the code, verify that it's working well using the testbench. In addition to the log, submit a waveform screenshot showing correct operation.

3. Full adder
Design a 1-bit full adder taking three 1-bit inputs: a, b, and ci, and giving sum and co.

module fulladder( sum, co, a, b, ci);
  input a, b, ci;
  output sum, co;

Write a testbench and use it to simulate the adder, checking all input combinations.

4. Four bit unsigned adder
Design a 4-bit unsigned adder using instantiation of four 1-bit adders.

module add4( sum, co, a, b, ci);
  input [3:0] a, b;
  input ci;
  output [3:0] sum;
  output co;

No need to write a testbench, since it will be tested as part of the next exercise.

5. Four bit add/sub unit

Use the 4-bit unsigned adder from the previous exercise to design a 4-bit signed add/sub unit, which can either add or sub based on a mode input (0 add, 1 sub).

module addsub( result, operand_a, operand_b, mode );
   input [3:0] operand_a, operand_b;
   input mode;
   output [3:0] result;

 Test it with the provided testbench, and submit a wave screenshot of the simulation.

6. Parity
Design a state machine which will accept a stream of bits (one every clock), and will output '1' if the number of ones accepted so far is even, or '0' otherwise.

module iseven(clk, in, reset, out);
   input clk, in, reset;
   output out;

Fill in the provided parity.v and parity_tb.v and submit them along with the Verilog log file.

7. Bi-Modal N-bit Saturating Counter
Design an N-bit saturating counter circuit, which is widely used for branch prediction. The circuit maintains an N-bit counter, initialized to 0 at reset=1. The counter value is preserved when reset=0 and branch=0, whereas it is updated when reset=0 and branch=1 according to the following rule:
       counter(t+1) = min{ counter(t) + 1, 2^N – 1} if taken == 1
       counter(t+1) = max{ counter(t) – 1, 0 } if taken == 0
The output prediction equals 1 if and only if counter(t) >= 2^(N-1)

module sat_count(clk, reset, branch, taken, prediction);
   parameter N=2;
   input clk, reset, branch, taken;
   output prediction;

Submit a state diagram of sat_count(N=2). Fill the sat_count.v code, and write a testbench sat_count_tb.v. Your test-bench must perform a test of sat_count(N=2) and print a final answer such as "PASSED ALL TESTS".

8. fifo(N,W)
Design a first-in-first-out queue synchronous module which satisfies the specifications below:

module fifo(clk, reset, in, push, pop, out, full);
   parameter N=4; // determines the maximum number of words in queue.
   parameter M=2; // determines the bit-width of each word stored in the queue.

   input clk, reset, push, pop;
   input [M-1:0] in;
   output [M-1:0] out;
   output full;

The functionality:
Let W(t)=<w1,w2,…,wn> denote the words stored at the module at time t, where 1,…,n corresponds to the chronological order of the words registered at the queue (n is the oldest). The outputs must respect the following behavior:
full(t) = 1 iff n=N
out(t) = wn iff n>0 (otherwise out(t)=0M)
W(t+1) = < > (empty queue) iff reset(t)=1
If reset(t)=0 then the functionality depends on n:
n=0:
W(t+1) = <in>	iff push(t)=1 and pop(t)=*
W(t+1) = W(t) iff push(t)=0 and pop(t)=*
0<n<N:
W(t+1) = <in, w1,w2,…,wn-1> iff push(t)=1 and pop(t)=1
W(t+1) = <in, w1,w2,…,wn> iff push(t)=1 and pop(t)=0
W(t+1) = <w1,w2,…,wn-1> iff push(t)=0 and pop(t)=1
W(t+1) = W(t) iff push(t)=0 and pop(t)=0
n=N:
W(t+1) = <in, w1,w2,…,wN-1> iff push(t)=1 and pop(t)=1
W(t+1) = W(t) iff push(t)=* and pop(t)=0
W(t+1) = <w1,w2,…,wN-1> iff push(t)=0 and pop(t)=1

Fill the fifo.v code, and write a testbench fifo_tb.v which instantiates fifo(4,2) module (set N,M to 4,2 from the test-bench using parameter overriding). Your test-bench must print a final answer such as "PASSED ALL TESTS".